Industrial Informatics and Embedded Systems -  November 30th 2017

Surname ................................…..                       Name .......................... Registration n° …………………………

- A 32 bit microprocessor with working frequency of 50 MHz must measure a pulse train frequency in the range [1Hz-1KHz] with +/- 1% precision. The processor must also supply the power to a resistive load with a precision equal to 0.4% and must acquire two BCD numeric values. No latency must be taken into account for interrupt tasks scheduling. The more accurate technique that allows a reasonable measurement production frequency of the pulses must be established considering the available number of bits.

- Calculate the latency time in a field bus featuring a microprocessor that transmits a command to a drive managed by a similar microprocessor that is located at a 500 m from it and at a velocity of 134400 Baud. Both the microprocessors use a USART serial interface for the transmission that is managed through an interrupt whose latency can be neglected. Both the microprocessors have a 300 MHz clock.

- What kind of function is performed by the code executed here below?

NB:

-the routine receives a value that is put in the r4 register.

-the results is provided in the r6 register

- Briefly answer to the following questions:

- Why in the HW-HW technique the latency affects the measurement production frequency and why not in the HW-Int?

- What kind of motivation bring to re-synchronise communication in asynchronous technique? Show an example.

- What kind of flags are set in the ARM processor if we perform the operation 231+1-1? And why?

- What kind of data structures for the data exchange among sender and receiver nodes are needed in a point2point half duplex serial communication protocol?

# Text boxes

start:		STRFD	r14, [r13]!

STRFD	r4, [r13]!

CMP	r4, #1

BGT	noexit

MOV	r6, #1

ADD	r13, #4

LDRFD	r15, [r13]!

noexit:	ADD	r4, #-1

AND	r4, #FFFE

MOV	r7, r4

CMP	r7, #0

BEQ	noexit

BL	start

LDRFD	r4, [r13]

LDRFD	r14, [r13]!

MUL	r6, r4, r6

MOV	r15, r14