Industrial Informatics and Embedded Systems -  January 31st 2018

Surname ................................…..                       Name .......................... Registration n° …………………………

- A 32 bit microprocessor with working frequency of 100 MHz must measure a pulse train frequency in the range [100 Hz-100 KHz] with +/- 1% precision. The processor manages a parallel IEEE488 communication protocol, charge two TBV values on two 4 bit counters and uses the remaining bits for measuring the frequency of the pulses. The more accurate technique that allows the best precision in the measurement if the frequency of the pulses must be established considering the available resources. Neglect the interrupt latency.

- What kind of function is performed by the code executed here below?

.datasegment

dati1:	.byte	10, -20, -40

ord1:	.space	804

co_1:	.space	8

.codesegment

sub1:	MOV	r0, #-100

MOV	r2, #-1

EOR	r1, r2, r0

ADD	r1, r1, #1

ADR	r2, dati1

ADR	r9, co_1

ADR	r8, ord1

LDRB	r3, [R2]

LDRB	r4, [r2, #1]

LDRB	r5, [r2, #2]

mpt1:	MUL	r6, r0, r0

MUL	r6, r6, r3

MUL	r7, r0, r4

ADD	r6, r5, r6

ADD	r6, r6, r7

STR	r6, [r8]

CMP	r0, #-100

BGT	aft1

wr_1:	STR	r6, [r9, #4]

STR	R0, [r9]

cyc1:	ADD	r8, r8, 4

ADD	r0, r0, 1

CMP	r0, r1

BLE	mpt1

MOV	r15, r14

aft1:	LDR	r2, [r9, #4]

CMP	r6, r2

BLT	wr1

B	cyc1

NB:

- the directives code_segment and data_segment simply denote the beginning of the program (the code) and the beginning of the part devoted to data structures declaration. The directive space allocate N memory bytes to be filled with data.

- Briefly answer to the following questions:

- Why two adaptors in contact rotate with velocities whose ratio is the inverse of the radius?

- What is the relation between the mechanical power and the angular velocity in DC motor and why is that?

- What are the sources of delay when the MOS that drive the rotation of a step motor?

- In a typical USART port comment the use of the bit that control the Fifos and explain in what situations they can be useful or must be used

- Let’s suppose that two nodes communicating through the Can Bus have a distance equal to 200 m considering that the transmission is done at 5 Mb/s how long should be the Propagation Segment to compensate for the delay in the transmission?

- Considering the last question implement a circuit based on counters, prescaler and oscillators (suppose 1 MHz) able to measure the length of the Propagation Segment